## Slide 1
OL13
1st Line Maintenance – Opal Top Up and Single Trip Ticket Machine
Version 1.1
Notes: NOTE TO CURRICULUM DEVELOPER: REFER TO QTMS-PR-39 CURRICULUM DEVELOPMENT GUIDE ON THE USE OF THIS TEMPLATE.

## Slide 2: Course Outline
Purpose statement / Objective
  This course aims to equip participants with the required knowledge and skills to be able to undertake 1st line maintenance of Opal Top Up and Single Trip Ticket machines.
Learning Outcomes
  At the end of the course, participants will have learned how to:
    Describe the correct procedure for routine exterior cleaning
    Explain how to log in to the Opal Top Up and Single Trip Ticket machine maintenance software
    Explain how to check the status of consumables
    Describe how to open the Opal Top Up and Single Trip Ticket machine
    Identify hardware components of the Opal Top Up and Single Trip Ticket machine
    Describe how to replenish the paper receipt roll

## Slide 3: Course Outline
    Describe how to replenish Single Trip Tickets
    Explain how to close and lock Opal Top Up and Single Trip Ticket machines.
Assessment
  Participants will need to complete the following assessment:
    Practical Observation Assessment.

## Slide 4: Housekeeping
Mobile Phone Use
Evacuation Plan
Facilities
Put on Silent
Refer to wall chart in classroom
Location of main facilities
CCTV camera – filmed whilst on premises
Smoking – not on property
First Aid – box locations / officer on duty / defibrillator

## Slide 5: Housekeeping
Drug and Alcohol Policy (applicable to STA and TfNSW Staff) – You may be tested at any time
Injuries and Incidents – For all injuries and incidents that occur while at training, they must inform the following:
    Training Facilitator
    Supervisor
    Reporting
      RMS Injury Hotline – 1300 131 469
      STA complete Form 178 Injury / Incident Form
      TfNSW Injury Hotline – 1800 772 779
Reasonable Adjustment:
    Transport for NSW will treat each request for an adjustment because of a disability objectively and make any adjustments that are reasonable, necessary and possible. (Refer to Facilitator guide for full details)
Training Record Sheets
General housekeeping
Administration

## Slide 6: Topics we’re covering today
Topic 1: Routine exterior cleaning
Topic 2: Log in to Opal Top Up and Single Trip Ticket Machine maintenance software
Topic 3: Check status of consumables
1
2
3
Topic 4: Open Top Up and Single Trip Ticket Machines
4

## Slide 7: Topics we’re covering today
Topic 5: Replenish paper receipt roll
Topic 6: Replenish Single Trip Tickets
Topic 7: Close and lock Opal Top Up and Single Trip Ticket Machines
5
6
7
Topic 8: Assessment
8

## Slide 8: Opal Top Up and Single Trip Ticket Machines
  The Opal Top Up and Single Trip Ticket Machine is an automated ticket payment machine which comes in two styles:
    The Galexio Machine which allows customers to top up their Opal cards using credit/debit cards, buy Single Trip Tickets and view their Opal card balance.
    The Astreo Machine which allows customers to top up their Opal cards using cash or credit/debit cards, buy Single Trip Tickets and view their Opal card balance.
  There are slight differences in how you will perform your tasks and these will be highlighted throughout the training.

## Slide 9: Galexio Opal Top Up and Single Trip Ticket Machine
Exterior
Interior

## Slide 10: Astreo Opal Top Up and Single Trip Ticket Machine
Exterior
Interior

## Slide 11
TOPIC 1
Routine exterior cleaning

## Slide 12
  Complete visual check of machine cleanliness
  Assess cleaning requirements for dust, grime or graffiti
  Clean dust with an air Duster or cleaning cloth
  Clean grime and graffiti with anti-static cleaning foam spray such as Carterclene
Clean exterior of Opal Top Up and Single Trip Ticket Machine

## Slide 13
TOPIC 2
Log in to Opal Top Up and Single Trip Ticket Machine maintenance software

## Slide 14: Engineering Maintenance Software Login/Access
The staff member must have the following to enable access to the Engineering Maintenance Software (EMS) on the Opal Top Up and Single Trip Ticket Machine:
  The door lock key
  Latch lifting tool for Astreo Machine
  4-digit Agent Number
  4-digit Secret Code

## Slide 15
  Push latch down on the top right hand inside of the paper receipt tray to allow the lock to be visible (see inset – latch is “flush” against the frame)
Not visible
Visible
Log In – Galexio Machine

## Slide 16
  Insert key into lock and turn left 90 degrees* until the keypad is shown on the display ** If opening the door is required, a 180 degree turn will fully unlock the lock
Log In – Galexio Machine

## Slide 17
  The Opal Top Up and Single Trip Ticket Machine prompts the staff member to enter their 4-digit AGENT NUMBER The number positions are dynamic – they move each time a digit is pressed.
Log In – Galexio Machine

## Slide 18
  The Opal Top Up Machine prompts the staff member to enter their 4-digit SECRET CODE Note: Three attempts are allowed to enter the correct pair of codes before an alarm is sounded.
Log In – Galexio Machine

## Slide 19
  The Opal Top Up Machine will display Servicing – Maintenance is starting...
Log In – Galexio Machine

## Slide 20
  If sign-on is successful, the Opal Top Up and Single Trip Ticket Machine displays the MAINTENANCE Software screen (main menu)
Log In – Galexio Machine

## Slide 21
  On top lock*, use the supplied tool to raise latch to allow the lock to be visible
  Insert key into lock and turn left 90 degrees** until the keypad is displayed
Not visible
Visible
*Always open the top lock first
** If opening the door is required, a 360 degree turn will fully unlock the lock
Log In – Astreo Machine

## Slide 22
  The Opal Top Up and Single Trip Ticket Machine prompts the staff member to enter their 4-digit AGENT NUMBER The number positions are dynamic – they move each time a digit is pressed.
Log In – Astreo Machine

## Slide 23
  The Opal Top Up Machine prompts the staff member to enter their 4-digit SECRET CODE Three attempts are allowed to enter the correct pair of codes before an alarm is sounded.
Log In – Astreo Machine

## Slide 24
  The Opal Top Up Machine will display Servicing – Maintenance is starting...
Log In – Astreo Machine

## Slide 25
  If sign-on is successful, the Opal Top Up and Single Trip Ticket Machine displays the MAINTENANCE Software screen (main menu)
  Remove key and stow in a safe place
Log In – Astreo Machine

## Slide 26
TOPIC 3
Check status of consumables

## Slide 27: Check consumables for Paper Receipt Status
    Select Maintenance Functions

## Slide 28: Check consumables for Paper Receipt Status
    Select Maintenance of Iml5 printer The IML5 printer is the paper receipt printer

## Slide 29: Check consumables for Paper Receipt Status
    Select View Status

## Slide 30
    Status displays. In this example Stock=381886mm
    Touch anywhere to return to previous menu
    Select Previous Menu
    Select Previous Menu
Check consumables for Paper Receipt Status

## Slide 31: Check Consumables for Single Trip Ticket Status
    Select Maintenance Functions

## Slide 32: Check Consumables for Single Trip Ticket Status
    Select Maintenance of Ims printer IMS Printer is the Single Trip Ticket printer

## Slide 33: Check Consumables for Single Trip Ticket Status
    Select View Status

## Slide 34: Check Consumables for Single Trip Ticket Status
    Status displays. In this example Stock1=1002 tickets left in the box.
    Press anywhere to return to previous menu.
    Select Previous Menu.
    Select Previous Menu.
    Note full stock for each box is 1200 tickets.

## Slide 35
TOPIC 4
Open Top Up and Single Ticket Machines

## Slide 36: Open the Galexio Machine
  Open the door until the bracket clicks into place at the base of the door
  Remove the key and stow in a safe place

## Slide 37: Open the Astreo Machine
  Remove the key from the top lock if not already done so
  Use the supplied tool to raise up the latch for the bottom lock

## Slide 38: Open the Astreo Machine
  Insert key into keyhole and turn fully anti-clockwise to unlock the bottom four bolts
  Open the door until the latch clicks at the base of the door
  Remove key and stow in a safe place

## Slide 39: Open the display inside
  Unlatch the display by pressing the lever down and lifting slightly over latch and open fully

## Slide 40: Open the display inside
  Display is now visible while working inside Use the key pad whilst display is open, using the arrow keys to navigate and Enter to confirm.

## Slide 41
TOPIC 5
Hardware components of the Opal Top Up and Single Trip Ticket Machines

## Slide 42: Door
    The door bracket (1) secures the door in the open position
    The display (2) opens while the door is open by pressing the latch
    Use the keypad (3) to operate the display while the display is open
1
2
3

## Slide 43: Receipt Printer
    Paper receipt printer (1) is located on the left hand side, with the paper receipt roll placed on top
1

## Slide 44: Single Trip Ticket Printer
    The single trip ticket printer (1) is directly to the right of the paper receipt printer
    Blank tickets (2) are loaded through ticket slots under the printer
1
2

## Slide 45: Coin Module (Astreo Machine only)
    The coin hopper (1) holds and dispenses coins
    The coin vault (2) stores coins for collection by Cash Collection Agents
1
2

## Slide 46: Note Module (Astreo Machine only)
    The note reader (1) receives and scans notes to determine denomination
    The note vault (2) stores notes
    The note loader (3) replenish note recyclers
    Note recyclers (4) dispense notes
1
2
3
4

## Slide 47: Duress Alarm - Galexio Machine
    Press alarm (1) if under threat or a robbery is underway Alarm will operate for time predetermined by Transport for NSW
1

## Slide 48: Duress Alarm - Astreo Machine
    Press alarm (1) if under threat or a robbery is underway Alarm will operate for time predetermined by Transport for NSW
1

## Slide 49
TOPIC 6
Replenish paper receipt roll

## Slide 50: Replenish paper receipt roll - Galexio Machine
    Select Maintenance Functions

## Slide 51: Replenish paper receipt roll - Galexio Machine
    Select Maintenance of Iml5 printer The IML5 printer is the paper receipt printer

## Slide 52: Replenish paper receipt roll - Galexio Machine
    Select Reload Paper

## Slide 53: Replenish paper receipt roll - Galexio Machine
    Select Support RECEIPT (RECEIPT)

## Slide 54: Replenish paper receipt roll - Galexio Machine
    The Opal Top Up and Single Trip Ticket Machine will display the Support RECEIPT (RECEIPT) IML5 screen
    Now it is time to access the IML5 (paper receipt) printer
    Lock display back into place

## Slide 55: Replenish paper receipt roll - Galexio Machine
    Pull out paper from printer
    Lift up silver paper guide in front of paper receipt roll spindle

## Slide 56: Replenish paper receipt roll - Galexio Machine
    Once the silver paper guide is pushed up you can now rotate the metal paper guide downwards and towards you
    The paper receipt roll is now able to be removed
    Remove the empty spindle and remove the empty paper receipt roll from it

## Slide 57: Replenish paper receipt roll - Galexio Machine
    Unpack new paper receipt roll and tear off the first layer or so to ensure that there is no glue or sticky residue on the paper

## Slide 58: Replenish paper receipt roll - Galexio Machine
    Insert spindle into new paper receipt roll

## Slide 59: Replenish paper receipt roll - Galexio Machine
    Ensure the replacement paper receipt roll end is facing forward and feeding from the top

## Slide 60: Replenish paper receipt roll - Galexio Machine
    Slide the paper receipt roll into the slot

## Slide 61: Replenish paper receipt roll - Galexio Machine
    Rotate silver paper guide back up until latch locks back into place

## Slide 62: Replenish paper receipt roll - Galexio Machine
    Feed the paper into the printer guide as far as possible You should see the paper appear in the small cutout window bottom right.

## Slide 63: Replenish paper receipt roll - Galexio Machine
    Unlatch the display by pressing the lever down and lifting slightly over latch and open fully Use the arrow buttons on the keypad to navigate the display

## Slide 64: Replenish paper receipt roll - Galexio Machine
    Select Paper Guiding

## Slide 65: Replenish paper receipt roll - Galexio Machine
    Select New Roll. The paper will automatically be pulled down into printer

## Slide 66: Replenish paper receipt roll - Galexio Machine
    The display will briefly show “Printing test ticket”
    Collect and check test paper receipt

## Slide 67: Replenish paper receipt roll - Galexio Machine
    Display refreshes. “Reload done. Test ticket printed” message will display
    Press Enter

## Slide 68: Replenish paper receipt roll - Galexio Machine
    Maintenance of IML5 displays IML5 printer is the paper receipt printer
    Select Previous Menu
    Select Previous Menu

## Slide 69: Replenish paper receipt roll - Galexio Machine
    Main menu will display

## Slide 70: Replenish paper receipt roll - Astreo Machine
    Select Maintenance Functions

## Slide 71: Replenish paper receipt roll - Astreo Machine
    Select Maintenance of Iml5 printer LML5 Printer is the paper receipt printer

## Slide 72: Replenish paper receipt roll - Astreo Machine
    Select Reload Paper

## Slide 73: Replenish paper receipt roll - Astreo Machine
    Select Support RECEIPT (RECEIPT)

## Slide 74: Replenish paper receipt roll - Astreo Machine
    The Opal Top Up and Single Trip Ticket Machine will display the Support RECEIPT (RECEIPT) IML5 screen IML5 printer is the paper receipt printer
    Now it is time to access the printer
    Lock display back into place

## Slide 75: Replenish paper receipt roll - Astreo Machine
    Press lever at bottom right of paper receipt printer towards you and lift down

## Slide 76: Replenish paper receipt roll - Astreo Machine
    The paper receipt roll is now able to be removed
    Lift up and remove empty spindle reel from printer and remove empty roll

## Slide 77: Replenish paper receipt roll - Astreo Machine
    Unpack new paper receipt roll and tear off the first layer or so to ensure that there is no glue or sticky residue on the paper

## Slide 78: Replenish paper receipt roll - Astreo Machine
    Insert spindle into new paper receipt roll

## Slide 79: Replenish paper receipt roll - Astreo Machine
    Ensure the replacement paper receipt roll end is facing forward and feeding from the top

## Slide 80: Replenish paper receipt roll - Astreo Machine
    Slide the paper receipt roll into the slot

## Slide 81: Replenish paper receipt roll - Astreo Machine
    Raise printer module back up as far as it goes and press lever towards you to lock into place

## Slide 82: Replenish paper receipt roll - Astreo Machine
    Feed the paper into the printer guide as far as possible You should see the paper appear in the small cutout window bottom right.

## Slide 83: Replenish paper receipt roll - Astreo Machine
    Unlatch the display by pressing the lever down and lifting slightly over latch and open fully Use the arrows on the keypad to navigate on the display.

## Slide 84: Replenish paper receipt roll - Astreo Machine
    Select Paper Guiding

## Slide 85: Replenish paper receipt roll - Astreo Machine
    Select New Roll The paper will automatically be pulled down into printer.

## Slide 86: Replenish paper receipt roll - Astreo Machine
    The display briefly will display “Printing test ticket”
    Collect and check test paper receipt

## Slide 87: Replenish paper receipt roll - Astreo Machine
    Display refreshes. “Reload done. Test ticket printed” message will display
    Press Enter

## Slide 88: Replenish paper receipt roll - Astreo Machine
    Maintenance of IML5 displays
    Select Previous Menu
    Select Previous Menu

## Slide 89: Replenish paper receipt roll - Astreo Machine
    Main menu will display

## Slide 90
TOPIC 7
Replenish Single Trip Tickets

## Slide 91: Replenish Single Trip Ticket Stock - Galexio Machine
    Select Maintenance Functions from the Main Menu

## Slide 92: Replenish Single Trip Ticket Stock – Galexio Machine
    Select Maintenance of Ims printer IMS Printer is the Single Trip Ticket printer

## Slide 93: Replenish Single Trip Ticket Stock - Galexio Machine
    Select Reload Paper

## Slide 94: Replenish Single Trip Ticket Stock - Galexio Machine
    Select Support SCC (SCC) SCC is the Single Trip Ticket module

## Slide 95: Replenish Single Trip Ticket Stock - Galexio Machine
    Select the appropriate stock to replenis
      (either stock 1 or stock 2 although 1-4 displays)

## Slide 96: Replenish Single Trip Ticket Stock - Galexio Machine
    Read instructions
    Lock display back into place

## Slide 97: Replenish Single Trip Ticket Stock - Galexio Machine
    Pull out printer towards you
    Remove empty box and discard

## Slide 98: Replenish Single Trip Ticket Stock - Galexio Machine
    There are 2 ticket stock slots that can be used Start at Slot 1 for back box and 2 for front.

## Slide 99: Replenish Single Trip Ticket Stock - Galexio Machine
    Open up new box by tearing along the perforated edges at top of box

## Slide 100: Replenish Single Trip Ticket Stock - Galexio Machine
    Ensure new box has Opal logo on the left hand side at the bottom with white facing forward and place in tray

## Slide 101: Replenish Single Trip Ticket Stock - Galexio Machine
    Open display
    Select Paper Advance to allow Single Trip Tickets to be fed into the printer

## Slide 102: Replenish Single Trip Ticket Stock - Galexio Machine
    You will hear the printer ready to grab the stock.
    Feed the ticket stock through the slot – 1 and 2. The printer will grab tickets.

## Slide 103: Replenish Single Trip Ticket Stock - Galexio Machine
    Paper advance displays
    Use the keypad to select new Roll

## Slide 104: Replenish Single Trip Ticket Stock - Galexio Machine
    Display refreshes and will show Edited test Ticket green box
    Press Enter

## Slide 105: Replenish Single Trip Ticket Stock - Galexio Machine
    Test ticket will drop from printer into the base of the machine

## Slide 106: Replenish Single Trip Ticket Stock - Astreo Machine
    From the Maintenance of IMS Printer screen, select Reload Paper on the keypad IMS printer is the Single Trip Ticket printer

## Slide 107: Replenish Single Trip Ticket Stock - Astreo Machine
    Select Support SCC (SCC) on the keypad SCC is the Single Trip Ticket module.

## Slide 108: Replenish Single Trip Ticket Stock - Astreo Machine
    Use the keypad to select the appropriate stock to replenish

## Slide 109: Replenish Single Trip Ticket Stock - Astreo Machine
    Instructions will display
    Lock Display back into place to clear the way for removal of the printer

## Slide 110: Replenish Single Trip Ticket Stock - Astreo Machine
    Pull out printer towards you
    Lift up guard that holds the boxes in place – by lifting front first. Remove guard and place on ground in a safe place
    Remove empty box and discard

## Slide 111
    There are three ticket stock slots that can be used Start at Slot 1 for back box, then 2 and 3.
Replenish Single Trip Ticket Stock - Astreo Machine

## Slide 112: Replenish Single Trip Ticket Stock - Astreo Machine
    Open up new box by tearing along the perforated edges at top of box

## Slide 113: Replenish Single Trip Ticket Stock - Astreo Machine
    Ensure new box has Opal logo on the left hand side at the bottom with white facing forward and place in tray

## Slide 114: Replenish Single Trip Ticket Stock - Astreo Machine
    Open display
    Select Paper Advance

## Slide 115: Replenish Single Trip Ticket Stock - Astreo Machine
    You will hear the printer ready to grab the stock
    Feed the ticket stock through the slot – 1, 2 or 3. The printer will grab tickets.

## Slide 116: Replenish Single Trip Ticket Stock - Astreo Machine
    Paper advance displays
    Select new Roll

## Slide 117: Replenish Single Trip Ticket Stock - Astreo Machine
    Display refreshes and will display Edited test Ticket green box
    Press Enter

## Slide 118: Replenish Single Trip Ticket Stock - Astreo Machine
    Test ticket will drop from printer

## Slide 119: Replenish Single Trip Ticket Stock - Astreo Machine
    Replace the guard back by hooking the back section first and then the front
    Slide the guard down until it locks into place

## Slide 120: Replenish Single Trip Ticket Stock - Astreo Machine
    Push the printer back into the Opal Top Up and Single Trip Ticket Machine and open the montior

## Slide 121: Replenish Single Trip Ticket Stock - Astreo Machine
    Select Previous Menu until you return to the main menu

## Slide 122: Empty IMS reject bin
    Select Maintenance Functions

## Slide 123: Empty IMS reject bin
    Select Maintenance of Ims printer IMS Printer is the Single Trip Ticket printer

## Slide 124: Empty IMS reject bin
    Select Empty IMS reject bin IMS reject bin is the Single Trip Ticket reject bin
    Select YES

## Slide 125: Empty IMS reject bin
    Display refreshes and will show instructions

## Slide 126: Empty IMS reject bin
    Pull latch forward to allow the black printer door to open

## Slide 127: Empty IMS reject bin
    Remove rejected tickets from bin and discard
    Close printer door
    Slide printer back into place

## Slide 128: Empty IMS reject bin
    Open display and use keypad
    Press Enter

## Slide 129: Empty IMS reject bin
    Dumped Sequestration displays
    Press Enter
    Select Previous Menu
    Select Previous Menu

## Slide 130
TOPIC 8
Close and lock Opal Top Up and Single Trip Ticket Machine

## Slide 131: Return Machine to Sales Mode
    Main Menu will display
    Select To Sales WITHOUT Reboot and press Enter

## Slide 132: Return Machine to Sales Mode
    Are you sure to return to sales WITHOUT reboot? message will display
    Select YES then press Enter

## Slide 133: Return Machine to Sales Mode
    Display refreshes. It is now time to put the display back in place and make sure the latch is on

## Slide 134: Close Door
    Use foot to gently lift the lock bracket at bottom of door then close the door
Galexio
Astreo

## Slide 135: Lock Opal Top Up and Single Trip Ticket Machine - Galexio Machine
    Push latch on front top right hand inside of the paper receipt tray down to allow the lock to be visible
    Close and lock the Opal Top Up and Single Trip Ticket Machine door by turning key fully clockwise
    Remove the key and store in a safe place

## Slide 136: Lock Opal Top Up and Single Trip Ticket Machine - Galexio Machine
    Display updates

## Slide 137: Lock Opal Top Up and Single Trip Ticket Machine - Galexio Machine
    The temporary close message is displayed briefly before returning to the Customer Home Screen

## Slide 138: Lock Opal Top Up and Single Trip Ticket Machine - Galexio Machine
    Opal Top Up and Single Trip Ticket Machine is now back in Sales Mode

## Slide 139: Lock Opal Top Up and Single Trip Ticket Machine - Astreo Machine
  On bottom lock, use the supplied tool to raise latch to allow the lock to be visible. Insert key into lock and turn fully clockwise
  On top lock, use the supplied tool to raise latch to allow the lock to be visible. Insert key into lock and turn fully clockwise
  Remove the key and store in a safe place

## Slide 140: Lock Opal Top Up and Single Trip Ticket Machine - Astreo Machine
    Display updates

## Slide 141: Lock Opal Top Up and Single Trip Ticket Machine - Astreo Machine
    The temporary close message is displayed briefly before returning to the Customer Home Screen

## Slide 142: Lock Opal Top Up and Single Trip Ticket Machine - Astreo Machine
    Opal Top Up and Single Trip Ticket Machine is now back in Sales Mode

## Slide 143
TOPIC 8
Assessment